## Slide 1
USE CASE 3 • REFERENCE ARCHITECTURE
Vendor-neutral architecture, with the safety layer out of reach
USERS & OPERATORS
Control room console
gas controllers
Operations copilot
engineers • planners
Mobile approvals
supervisors • step-up MFA
Compliance workspace
records • reviews
AGENTS
autonomy tier
Condition Monitoring
Tier 2 • scores
Diagnostics
Tier 1 • advises
Flow & Load Advisor
Tier 1 • proposes
Maintenance Planning
Tier 3 • notifications
Crew & Permit
Tier 2 • proposes
Compliance Records
Tier 2 • drafts
ORCHESTRATION
dedicated, federated
Operations Orchestrator
dedicated ops tier
Deterministic gates
approvals • confirmations
A2A delegation
internal agents
Event triggers
historian • alarms • orders
CONTROL PLANE
Registry
agents • tools • limits
AI gateway
LLM • MCP • A2A
Approval binding
exact change • 10 min
Cumulative limits
per hour • per shift
Identity
agent IDs • OBO
Safe defaults
stale data • kill switch
MODELS
routed by policy
Anomaly models
ML • time series
Hydraulic model
deterministic check
Fine-tuned SLM
self-hosted • text
Frontier LLM
private endpoint
MCP SERVERS & APIs
Historian replica
read • DMZ
Setpoint requests
gated write • DMZ
SAP S/4HANA
orders • parts
Workday
people • crews
Permits & quals
permit-to-work
Snowflake
sensor history
DATA GOVERNANCE
MDM & semantics
Asset master
stations • units
Tag master
tags to assets
Limits & MOC
read-only to agents
Glossary & lineage
tags to decisions
SYSTEMS OF RECORD
SCADA & historian
SAP S/4HANA
Workday HCM
Permit-to-work
GIS & assets
Snowflake
SAFETY & OT
independent
SIS & ESD
act on their own
Interlocks & relief
hardwired • mechanical
Control limits
engineering limits
Zones & conduits
IEC 62443
SECURITY AT EVERY LAYER
Phishing-resistant MFA
Per-agent identity
No agent path to safety
Bound, expiring approvals
Honeytokens & decoys
mTLS • TLS 1.3
HSM keys • AES-256
Tamper-evident logs
GOVERNANCE & OBSERVABILITY
Autonomy tiers & limits
Alert budget per controller
Stale-data safe defaults
Model risk validation
Control room management
OpenTelemetry traces
Kill-switch drills
Vendor-neutral: only systems of record are named products. Standards: endnotes 26, 27, 66, 68, 69, 90–94.
50
Notes: This is the vendor-neutral solution architecture, aligned to the north-star reference architecture, with one addition: a safety and OT layer beneath the systems of record that the agents cannot reach. Only the systems of record are named products.
Orchestration model selected: a dedicated orchestration tier for operations, federated under the enterprise control plane. Operations data and agents stay in the operator's own environment, close to the historian, while identity, policy, registry, audit and cost remain centrally governed. Orchestration is event-driven, with a supervisor pattern over A2A [27] and deterministic workflows for anything that touches equipment: a setpoint request always needs a controller's approval, and larger changes need a supervisor's confirmation.
Models and routing: anomaly models are conventional machine learning on time series. The operator's hydraulic model checks every proposed load shift deterministically and has the final word. A self-hosted small language model reads and drafts text, and a frontier model on a private endpoint summarizes diagnostics. Advice that rests on data that has since gone stale is discarded.
Control plane and policy: each approval is bound to the exact change and valid for ten minutes by the gateway's clock, with a supervisor as separate attester above a threshold. Cumulative caps limit flow re-allocation per hour and per shift across agents and sessions. Stale data (a feed more than 60 seconds old) drops the advisor to advice-only and voids pending requests, and alert budgets keep agent notifications within alarm-management limits. The binding and cumulative limits are custom Omni Gateway policies [78].
Security at every level: the design applies zero trust [90], with zones and conduits following ISA/IEC 62443 and NIST's OT security guide [68][69]. The only write path into operations is a setpoint-request service in the DMZ. Safety instrumented systems, emergency shutdown and interlocks stay independent of the agent path [66], and honeytokens and decoy tools in the DMZ flag any agent outside the governed path.
Credit: John Fisher, The AI Control Plane: Executive Briefing (2026), slide 50, licensed under CC BY-NC-ND 4.0: https://creativecommons.org/licenses/by-nc-nd/4.0/. The full deck, with its speaker notes and notices: https://johnfisher-ai.github.io/ai-control-plane-handbook/deck/. You may adapt this slide, with credit, under the additional permission in the deck’s notices: https://johnfisher-ai.github.io/ai-control-plane-handbook/deck/notices.html#permission.
Bracketed numbers in these notes, and endnote numbers on the slide, refer to the endnotes in Appendix B of The AI Control Plane Handbook: https://johnfisher-ai.github.io/ai-control-plane-handbook/handbook/appendix-b.html.