## Slide 1
USE CASE 3 • WRAP-UP
What the compressor use case proves
Agents can work in operational technology without weakening the safety case, if the control plane stops at the DMZ and people approve every change to equipment.
1
Agents propose and people with authority approve
Every change that reaches equipment needs a controller’s approval, bound to that exact change and valid for minutes.
2
The safety layer stays out of reach
Safety systems, interlocks and engineering limits act on their own, and no agent tool can touch them.
3
Limits add up, and stale data stops advice
Caps apply to the total change across agents and sessions. Stale data drops agents to advice-only.
4
One control plane, stopped at the DMZ
Every call is identified, authorized, observed and metered. Nothing crosses into operations except through a governed conduit.
NEXT STEP: A 90-DAY PILOT
01
Pick the scope
One segment of the compressor fleet. Baseline outages, effort and alert load.
02
Start read-only
Condition monitoring and diagnostics at Tier 1–2 on the historian replica.
03
Govern the traffic
Route every model and tool call through Agent Fabric and deploy the custom policies.
04
Then allow proposals
Add setpoint proposals with bound approvals once drills and evaluations prove out.
Confirm Runtime Fabric in the DMZ and connector coverage.
Sources: endnotes 66, 67, 78.
56
Notes: Wrap up with what this use case proves:
People with authority approve what agents propose. Every change that reaches equipment needs a controller's approval, bound to that exact change and valid for minutes, and larger changes need a supervisor as a separate attester.
The safety layer stays out of reach. Safety instrumented systems, emergency shutdown, interlocks and engineering limits act on their own. No agent tool can read or write safety logic, bypass an interlock or acknowledge a safety alarm [66][67].
Limits add up, and stale data stops advice. Cumulative caps apply across agents and sessions, and a stale feed drops agents to advice-only. The process falls back to its engineered safe state, not a blanket stop.
One control plane, stopped at the DMZ. Every call is identified, authorized, observed and metered, and nothing crosses into operations except through a governed conduit.
Proposed next step: a 90-day pilot. Scope one segment of the compressor fleet and baseline outages, effort and alert load. Start read-only with condition monitoring and diagnostics at Tier 1–2 on the historian replica. Route every model and tool call through Agent Fabric and deploy the custom Omni Gateway policies [78]. Add setpoint proposals with bound approvals only once kill-switch and approver drills and evaluations prove out.
Before committing dates, confirm Runtime Fabric deployment in the DMZ and connector coverage for the historian and permit systems.
Credit: John Fisher, The AI Control Plane: Executive Briefing (2026), slide 56, licensed under CC BY-NC-ND 4.0: https://creativecommons.org/licenses/by-nc-nd/4.0/. The full deck, with its speaker notes and notices: https://johnfisher-ai.github.io/ai-control-plane-handbook/deck/. You may adapt this slide, with credit, under the additional permission in the deck’s notices: https://johnfisher-ai.github.io/ai-control-plane-handbook/deck/notices.html#permission.
Bracketed numbers in these notes, and endnote numbers on the slide, refer to the endnotes in Appendix B of The AI Control Plane Handbook: https://johnfisher-ai.github.io/ai-control-plane-handbook/handbook/appendix-b.html.